## Slide 1: Medical Device and HIT System Integration Implications for healthcare quality, safety, and innovation
Julian M. Goldman, MD
Director, Program on Interoperability, Mass General Hospital
Medical Director, Partners HealthCare Biomedical Engineering
Anesthesiologist, MGH/Harvard Medical School
Contact information: www.jgoldman.info
Federal HIT Summit
Nov 20, 2014
Washington, DC

## Slide 2
1999 IOM published “To Err Is Human” up to 98,000 people a year die because of mistakes in hospitals.
2010 the Office of Inspector General for Health and Human Services said that bad hospital care contributed to the deaths of 180,000 patients in Medicare alone in a given year.
2013 Journal of Patient Safety: between 210,000 and 440,000 patients each year who go to the hospital for care suffer some type of preventable harm that contributes to their death.
“That would make medical errors the third-leading cause of death in America, behind heart disease, which is the first, and cancer, which is second. “
1999
2013
Notes: http://journals.lww.com/journalpatientsafety/Fulltext/2013/09000/A_New,_Evidence_based_Estimate_of_Patient_Harms.2.aspx
http://www.propublica.org/article/how-many-die-from-medical-mistakes-in-us-hospitals

## Slide 3
Devices, processes, non-integrated system  errors
Home ventilator
Notes: http://www.nwscape.com/brooke/images-new/icu-l.jpg
http://employees.csbsju.edu/lrodgers/images/baby%20icu.jpg
http://www.perfusion.arizona.edu/images/OR%20perfusion.jpg
http://www.fitsense.com/b/images/cardiac%20surgery%20cw.jpg

## Slide 4: OR scene – patient’s life saved: Clinicians need timely, accurate data to reduce error, treatment delays, injuries and deaths. Is that how we practice today? Where are innovative solutions?

## Slide 5
Pulse Oximeters measure oxygen saturation – displayed as SpO2 %
Julian M. Goldman, MD / MGH
Pulse Oximeter oxygen saturation is 84% on instrument display and in EHR
EMR
Medical Devices generate “First Mile” of data (from patient)
Blood Pressure
Bluetooth pulse oximeter
Notes: IoT – insert Nonin photo

## Slide 6
Example - Infusion technology:
Decision support?
Prevent contra-indicated infusion?
“Artificial pancreas” Capabilities? (closed loop)
Consolidate all data for adverse event analysis?
Check device status, software version? Recall?
Adjust settings remotely?
Medical Devices are also the “Last Mile”
(data back to devices)
These infusion pumps are for use on ONE patient

## Slide 7: In interdisciplinary settings, language matters …
Actual screen capture from intra-operative EMR during surgery
Julian M. Goldman, MD / MGH
Notes: Source – Metvision / MGH / Goldman

## Slide 8: Discrete, device-based alarms
Low SpO2 Alarm = 90%
Resp rate Alarm
< 8 or > 20
ETCO2 >x or <x?
Must function without context
Notes: Pulse ox simulator
http://vam.anest.ufl.edu/simulations/pulseoximeter.php
Capnogram
https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcSo2H8dY0xXmxgxs5B3AdzI9kmrYLFNywWcrcx1tTsR0eRa48ns2w

## Slide 9: Context-based “smart” alarms
Smart Alarm
Low SpO2 Alarm = 80%
Resp rate Alarm
< 8; CO2 > 60
EMR
Correct Time
Use trends
Data fusion
context
Is this an IOT approach? Maybe …
Notes: Pulse ox simulator
http://vam.anest.ufl.edu/simulations/pulseoximeter.php
Capnogram
https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcSo2H8dY0xXmxgxs5B3AdzI9kmrYLFNywWcrcx1tTsR0eRa48ns2w

## Slide 10: Pulse Oximeter Data example
Oxygen Level Low
WHY????
JM Goldman MD / MGH

## Slide 11: BP cuff - Pulse Oximeter Interaction
Not reall low oxygen
“Bad” data
JM Goldman MD / MGH
Baseline
Cuff inflates – loss of finger signal
Blood returns to finger

## Slide 12
Monitor Displays Low Oxygen Level (SpO2) Alarm Event “84%” at 2:07
No evidence of 84% SpO2 in EHR
(Blue ticks representing SpO2 values
Don’t change)
We must not discard data!!
Julian M. Goldman, MD / MGH
Notes: Data from Lunder OR 54 May 28 2013
JM Goldman MD

## Slide 13: Sources of variation in EHR documentation due to Data Sampling
Patient’s “actual” SpO2
minimum = 70%
60 Seconds
Example of possible EHR sample points for 1-minute recording
Based on this example,
EHR May record SpO2 as:
98%
92%
80%
75%
Etc.
Notes: Closest approximation of “actual” is pulse oximeter set to “beat-to-beat” mode, or 2-second averaging time.
Better data could be obtained from manufacturers proprietary data stream, but is not necessary for this study.

## Slide 14
Proposal: Can an Integrated Clinical Environment (ICE) add “error resistance” to healthcare delivery?
Notes: http://www.economist.com/news/special-report/21593583-proliferating-digital-platforms-will-be-heart-tomorrows-economy-and-even

## Slide 15: Standard for the “Integrated Clinical Environment” ASTM F2761-09
“Essential safety requirements for equipment comprising the patient-centric integrated clinical environment (ICE) — Part 1: General requirements and conceptual model”
Provides a standards-based system architecture intended to support safe interoperable medical systems
Recognized by FDA 8/2013: http://www.gpo.gov/fdsys/pkg/FR-2013-08-06/pdf/2013-19020.pdf
Notes: Developed by experts convened through MD PnP, TATRC BAA

## Slide 16
ICE Network Controller
Medical Device or
other equipment
Medical Device or other equipment
Medical Device or other equipment
ICE Supervisor (runs apps)
Apps for PCA Safety, Smart Alarms, Remote Notification, Team coordination
EMR
ICE Data Logger
Integrated Clinical Environment - Architecture
ICE System
Clinicians
Patient and Family
ICE External
Interface
From ASTM F2761-09
Standard recognized by FDA in August 2013
Notes: Patient Image: http://www.uofmmedicalcenter.org/healthlibrary/Article/88979
Clinician image: Icon from medicalappjournal.com

## Slide 17: OpenICE Open-Source Platform
Patient
PulseOx
Adapter
Network Controller
ICE Supervisor
Data
Logger
Caregiver
External
Network
Pump
Adapter
Patient Mon.
Adapter
Based on ASTM F2761 “Essential safety requirements for equipment comprising the patient-centric integrated clinical environment (ICE), IEEE 11073 nomenclature; OMG DDS pub/sub messaging middleware
Apps
Black Box
Recorder
www.openice.info
Notes: New version is built on open source implementation of open standards.
Open ICE equipment interfaces translate proprietary manufacturer-specific interfaces to common data representation and communication protocol
Better patient simulator allows patient algorithms to plug in
Devices are plug-and-play: any device that provides necessary interface can be used

## Slide 18
Apps for smart alarms; med safety; equipment management
What if…
Asking a lot of the platform
“Medical IoT”
(Internet of Things)
Notes: http://www.nwscape.com/brooke/images-new/icu-l.jpg
http://employees.csbsju.edu/lrodgers/images/baby%20icu.jpg
http://www.perfusion.arizona.edu/images/OR%20perfusion.jpg
http://www.fitsense.com/b/images/cardiac%20surgery%20cw.jpg

## Slide 19: Medical Device “Plug-and-Play” Interoperability Program (MD PnP)
Founded in 2004, the MD PnP research program is a multi-institutional community with Lab based at Massachusetts General Hospital (MGH), with grant support from NIH/NIBIB, NSF, DoD/TATRC, and NIST
Mission: lead the adoption of open standards and technologies for medical device interoperability to improve patient safety

## Slide 20: MD PnP Lab at MGH/PHS
Vender-neutral sandbox for experimenting with device interoperability solutions (standards technologies, products)
Contains devices – production and research
Supports diverse collaborators
Notes: Add lab funding
Better pictures

## Slide 21
www.openice.info
www.mdpnp.org